## Slide 1: GLUCOSE MONITORING WITH A METER
What Key Personnel Need To Know
Diabetes Care Tasks at School
Notes: The American Diabetes Association’s Diabetes Care Tasks at School: What Key Personnel Need to Know is a training curriculum that consists of PowerPoint modules with corresponding video segments, pre-/post-tests and other helpful resources.
This curriculum is based on and should be used in conjunction with the ADA’s Safe at School “Helping the Student with Diabetes Succeed: A Guide for School Personnel”. Training participants should read the ADA Safe at School Guide in conjunction with this training gain a better understanding of the requirements for appropriate school diabetes care. The ADA’s Safe at School Guide and other training resources may be found www.diabetes.org/sastraining.
Please refer to the Continuous Glucose Monitoring slide deck for details about CGM.
Some key points about the overall training:
Overall objective: The overall goal is to optimize safety, health, learning, and access for students with diabetes by providing diabetes education and training to school personnel o perform routine and emergency diabetes care tasks for students, under the supervision of a school nurse or another qualified health care professional. Completion of this training will help prepare school personnel to perform diabetes care tasks, ensuring that health needs are addressed in times and locations when a nurse is not available to provide needed care.
Rationale: The school nurse, when available, is the most appropriate person in the school setting to provide care for a student with diabetes. However, many schools do not have full-time nurses. Even for schools that do, the nurse may not always be available at all times during the school day, during school-sponsored extra-curricular activities or field trips to assist with routine care and emergency care. Trained school personnel must be available to perform and assist the student with diabetes care tasks.
PLEASE STATE: This presentation is not intended to provide legal or health care advice. Please consult with a legal or health care professional regarding your specific questions or needs.

## Slide 2: Optimal Student Health and Learning
Blood glucose (blood sugar) monitoring is a vital piece of the Diabetes Medical Management Plan (DMMP).
GOAL:
Notes: Each training component was created specifically for school nurses and other qualified health care professionals to train school personnel.
These components are:
• Diabetes Basics
• Diabetes Medical Management Plan
• Hypoglycemia
• Hyperglycemia
• Blood Glucose Monitoring
• Continuous Glucose Monitoring
• Glucagon Administration
• Insulin Basics
• Insulin by Syringe and Vial
• Insulin by Pen
• Insulin by Pump
• Ketones
• Nutrition and Physical Activity
• After-School Programs, Sports and Camps
• Before- and After- School Care
• Childcare
• Psychosocial Aspects
• Legal Considerations
• Type 2 Diabetes
This unit is Blood Glucose Monitoring.

## Slide 3: Learning Objectives
PARTICIPANTS WILL BE ABLE TO UNDERSTAND:
Why blood glucose is monitored
When blood glucose should be monitored
How to perform a blood glucose check
Required equipment
Notes: Participants will be able to understand:
Why blood glucose is monitored
When blood glucose should be monitored
How to perform a blood glucose check
Required equipment

## Slide 4
Blood Glucose Monitoring
Maintain blood glucose within target range
IMMEDIATE BENEFIT:
Maximize learning and participation
Identification, treatment, and prevention of lows and highs
LONG-TERM BENEFIT:
Decrease risk of long-term complications
Maximize health
CHALLENGE:
Many variables impact blood glucose
GOAL
Notes: Blood glucose monitoring is the cornerstone of diabetes care.
Goal: Maintain blood glucose within target range.
Immediate benefit: Identification, treatment, and prevention of high and low blood glucose levels. Maximize learning and participation.
Long-term benefit: Decrease risk of long-term complications. Maximize health.
Challenge: Many variables can impact blood glucose. These variables include insulin, food, activity, stress, injury, and illness.

## Slide 5
Role of the School
Facilitate blood glucose monitoring (BGM)
Document results of BGM when assistance or supervision is provided
Act on blood glucose check results
Communicate BGM results to parent/guardian or school nurse to monitor for trends
In accordance with Diabetes Medical Management Plan (DMMP):
Notes: The Diabetes Medical Management Plan (DMMP) is covered in greater detail in the unit on Diabetes Medical Management Plans. The DMMP is the document that will specify in detail the student’s diabetes needs at school.
Educational plans such as a 504 Plan, an Individualized Education Program (IEP) or the Individualized Health Care Plan (IHP) will elaborate on who does what tasks and where these tasks take place.
With respect to blood glucose monitoring the school should expect to:
Facilitate blood glucose monitoring by:
  allowing self-managing students to check their own blood glucose anywhere and anytime with provider and parent/guardian approval
  performing the check and/or providing direct assistance and supervision to those who need help
Act on the results of blood glucose checks in accordance with directives in the DMMP
Document results of blood glucose monitoring when assistance or supervision is provided
Communicate blood glucose results to parent/guardian or school nurse to monitor for trends per DMMP

## Slide 6
Benefits of diabetes self-management for capable students:
Improved blood glucose control
Safer for students
Students gain independence
Less stigma
Less time out of class
Assists decision making in response to blood glucose result
Test and treat anywhere/anytime. Does not need to go to the nurse.
Any Time, Any Place Monitoring
Notes: Who/what determines if the student is capable of self-management and can check own glucose levels?
A determination regarding individual capacity for self-management is jointly made by the student, his/her parent/guardian and his/her health care provider – all in collaboration with the school nurse.
What are the advantages of checking blood glucose levels any time and any place?
The student can achieve improved blood glucose control to prevent long-term complications of high blood glucose and complications of acute low blood glucose levels.
It is safer for student because less time is lost between recognizing symptoms, confirming low blood glucose, and obtaining treatment with a fast-acting sugar source followed by a snack or meal.
The student gains independence in diabetes management when the blood glucose meter is easily accessible and checks can be conducted as needed.
The student experiences less stigma as blood glucose monitoring loses its mystery when handled as a regular occurrence.
Students with diabetes who check their blood glucose levels in the classroom spend less time out of class.
Self-checking blood glucose levels helps students to learn and understand decision making process in taking the appropriate response to a blood glucose reading result.

## Slide 7
Simply, easy to use
Small meters
Reliable results (with smaller samples)
Options for alternate (to finger stick) site testing
Enhanced electronic functions to record, share, and analyze data
Many students use Continuous Glucose Monitoring (CGM) – see CGM module for specific information
Limitation of using meters: Unknown blood glucose between checks
Blood Glucose Monitoring Technology
Notes: Blood glucose monitoring with a meter continues to become more simple and more reliable.
The meters have gotten considerably smaller, making it easy for students to carry them from one school setting to another.
Additionally, reliability with a very small sample size has improved greatly. Whereas it formerly took a large drop of blood to get a valid blood glucose reading, now the strips actually wick in the blood.
The computer technology within the meters allow individuals to track insulin doses and food intake along with blood glucose results. These data can be downloaded to home or clinic computers for further analysis.
Yet with all this progress, monitoring still requires repeated “pokes” (5-6 times a day, sometimes more)
Limitation of using meters – don’t know blood glucose between checks.
Between samplings, students must rely on their body signals to tell them whether their blood glucose level is out of target range.
Many students use Continuous Glucose Monitoring (CGM) – see CGM module for specific information

## Slide 8
How it works:
A tiny glucose-sensing device called a "sensor" is inserted just under the skin and remains for 7–14 days
The sensor measures glucose in the tissue and sends the information to a receiver
Receiver = Manufacturer-issued display device, smart device, or insulin pump
The system automatically records a glucose value every 1–5 minutes
Some CGMs provide alarms to signal when glucose is out of target range
What is a Continuous Glucose Monitor (CGM)?
Notes: In the past few years considerable progress has been made in the continuous monitoring of glucose levels. The steps on the screen explain the basics of how the continuous glucose monitoring or CGM technology works:
A tiny glucose-measuring device called a "sensor" is inserted just under the skin.
The sensor measures glucose in the tissue fluids several times a minute and sends the information to a phone-sized device.
The system automatically displays and records an average glucose value every one to five minutes and is worn for multiple days with duration depending on the manufacturer.
The state of the continuous monitoring technology is such that finger stick checks are still required at times for either calibration or treatment decisions. Glucose monitoring instruction will be outlined in the student’s DMMP.
Most CGM have alarms that signal when glucose is out of target range.
While continuous glucose monitors are becoming more common, they are still not used for all students with diabetes. Some individuals use them daily while others for a short period to give the health care providers a picture of what is happening with glucose levels between monitoring times, particularly after meals and at night while sleeping.

## Slide 9
Some CGMs are indicated for treatment decisions—but not all
Blood glucose levels should be monitored with a blood glucose meter in accordance with the student’s DMMP
Use fingerstick or CGM?
Notes: A student who wears a continuous glucose monitor to school still needs to check blood glucose with a regular meter before treatment; unless specifically stated otherwise in the DMMP. Not all CGM are FDA approved for treatment decisions; use CGM in accordance with the student’s DMMP.
More specific procedures for continuous glucose monitoring (CGM) will be covered in another separate unit on CGM.

## Slide 10: Basic Steps
Know the target range per DMMP
Check at times specified in DMMP
Take immediate action—administer treatment to get back within target range
Notes: Basic Steps to using glucose monitoring as a TOOL.
Know the target range. Each student’s target range should be clearly identified in the DMMP.
Check at times specified in DMMP.
Immediate Action – Treatment to get back within target range.

## Slide 11
DMMP specifies for an individual student
Regularly scheduled checks:
Routine monitoring before meals and snacks
Before, during, and/or after physical activity
Before dismissal
When to check?
Notes: Blood Glucose Checking
Regularly Scheduled checks
Routine monitoring before meals and snacks as per DMMP
Before, during, and after physical activity

## Slide 12
Per DMMP, extra checks may be necessary:
Hypoglycemia or hyperglycemia symptoms
Change in diabetes management
Periods of stress or illness
Prior to academic tests
Early or delayed release from school
CGM alarms
When else to check?
Notes: There are times when a student needs to check blood glucose more often than usual, including the following
When low or high blood glucose is suspected, either because the student is symptomatic or the adult observes symptoms.
During periods of stress or illness
Prior to academic tests
When there are changes made in the management program - such as a change in medication doses, meal plan, or physical activity.
Early or delayed release from school (e.g. inclement weather)
When the CGM alarms
The conditions for performing non-routine blood glucose checks should be specified in the DMMP. Generally, the student and/or parent/guardian will determine if/when additional blood glucose checks are required based on specific symptoms or concerns.
Teachers are encouraged to bring concerns about frequency of blood glucose checks to the attention of the school nurse, student, parent/guardian, and/or health care providers as appropriate.

## Slide 13
Lancing Devices
Lancets
Pen-Type Lancing Devices
FastClix
Notes: The basic tool for drawing blood for a glucose check is the lancet, a very small, sharp needle in a plastic sleeve. There are many types of lancets and lancet devices.
Many students will use a lancing device, a pen-shaped lancet holder that "launches" the needle with a spring and controls the depth of the puncture. Some lancing devices (like the one pictured at the bottom of the screen) have several depth settings to allow for the difference between sensitive fingers and callused fingers. Some come with two caps for the end that touches the finger to adjust the depth of puncture. In addition, the pressure of the finger on the cap determines how deep the puncture will go. It should be deep enough to provide an adequate amount of blood, but not be so deep as to cause bruising or pain.
If possible, allow the student to remove the lancet to avoid accidental contact to an exposed sharp by school staff. Lancets should be disposed of after use in a sharps disposal container as per parent’s/guardian’s agreement with school and local ordinances.
Some students may use a multiple fingerstick device that has a self-contained, six-lancet drum, shown in picture at right.
NEVER USE ONE STUDENT’S LANCING DEVICE ON ANYONE ELSE.

## Slide 14
Features vary:
Sample size
Test time—how long it takes to get results
Alternate-site testing capacity
Communication with other devices—pumps, CGMs
Become familiar with operation of meter using 1-800 number on back of meter
Knowing the Meter
Notes: There are many reliable meters on the market. Each has a unique set of features and operating procedures.
A number of features vary from meter to meter. Some of the features are convenience-based. Others can be critical to accuracy of results.
Sample size needed
Wait time
Alternate-site testing capacity
Work with parent/guardian or school nurse to become familiar with the operation of student’s particular meter. Or if not available, blood glucose meters have a 1-800 number on the back to call for questions about meter and to obtain technical support. Also, manufacturers’ website have videos, demos, and user guides that may be downloaded.

## Slide 15
Preparation
Gather blood glucose monitoring supplies:
Lancet
Test strips
Meter
Student washes and dries hands thoroughly
If assisting or performing for student, put on disposable gloves
1
2
3
Notes: Instructions:
1. Gather blood glucose monitoring supplies:
lancet
test strip
meter
2. Student washes hands and dries thoroughly.
3. If assisting or performing for student, put on disposable gloves.

## Slide 16
Readying the Meter
Turn the meter on
Check code # (if required)
Insert a strip into the meter
4
5
6
Notes: Instructions:
4. Turn the meter on if necessary. Some meters turn on automatically when the strip is inserted.
5. Check code number that appears on meter with the code number found on the container of the test strips. Many meters today may not require this step; however, if used accuracy depends on using the correct code. Correct meter code if codes do not match.
6. Insert a strip into the meter (some meters turn on automatically when the strip is inserted).

## Slide 17
Lancing the Finger
Hold the lancet device to the side of the finger and press the button to stick the finger.
Alternative site (per DMMP)
The school nurse and/or parent/guardian will give further instructions which sites are appropriate
Note: In the case of suspected hypoglycemia, only the finger should be used for blood glucose sampling
7
Notes: Instructions:
Hold the lancet device to the side of the finger and press the button to stick the finger. Use the side of the finger, as the tip and pad of the finger have more sensitive nerve endings. Express an adequate drop of blood.
If an alterative site is used (per DMMP), the school nurse and/or parent/guardian will give further instructions on the appropriate sites.
Note: In the case of suspected hypoglycemia, only the finger should be used for blood glucose sampling.

## Slide 18
Lancing the Finger
Follow instructions included with the meter when applying blood to strip
8
Drop,
not smear
Cover ALL of test strip window
Some strips wick blood onto the strip
Notes: Instructions:
8. How blood is applied to the strip is a little different from meter to meter.
Follow instructions included with the meter in how to apply the blood sample. This slide shows three different kinds of strips to illustrate some things to keep in mind.
With the first type of meter & strip, on the left: Be sure to drop, do not smear the blood onto the strip.
With all meters and strips, be sure to completely cover the test strip window.
The picture on the right illustrates that some strips actually wick the blood onto the strip by capillary action upon contact with the drop of blood on the finger (or other alternate site).

## Slide 19
Results
Wait until blood glucose results displayed
Dispose of lancet and strip
Record blood glucose results, take action per DMMP (connected meters may data transfer)
9
10
11
Notes: Instructions:
9. Wait. Blood glucose results will be displayed on the meter. Meter processing times vary. Most will take from 5 to one minute.
10. Dispose of the lancet in as per parent’s/guardian’s agreement with school and local ordinances. Never recap. Test strips may be discarded in a regular trash can.
Plan for Disposal of Materials That Come Into Contact with Blood
Blood glucose monitoring does not present a danger to other students or staff members when there is a plan for proper disposal of lancets and other materials that come into contact with blood.
The school health team should agree on the plan, which should be consistent with standard precautions and local waste-disposal laws. Disposal of sharps may be in a container kept at school or in the student’s personal container—a heavy-duty plastic or metal container with a tight-fitting lid. Used blood glucose test strips and other materials may be discarded in the regular trash. Check with the student’s personal diabetes health care team about health and safety requirements in your area.
11. Record blood glucose result and take action as per DMMP.

## Slide 20
Check manual
Contact manufacturer (1-800 or website)
What Does the Display Mean?
Notes: Meters do not only display numbers.
Some display “Lo” or “Hi” for out of range readings.
Some of them also display specific “error codes” that may indicate problems like an insufficient blood sample or that the temperature is out of range. You will need the meter manual to respond to these error codes.
You can get information about a specific meter and test strips from several different sources.
A copy of the manufacturer’s manual for the meter should be provided by the parent/guardian and kept in the health office for troubleshooting.
The user manual (and in some cases the meter itself) will include a toll-free number in case you have questions or problems.
Also, most meter companies now have their manuals available for download on their websites.

## Slide 21
Reference student’s target range
  Individualized for student
  May vary throughout day
  Take action per DMMP
Communicate sensitively-do not use “good” or “bad,” but rather communicate the actual value
Recognize value may vary according to time since eating, insulin, or physical activity
What Does the Number Mean?
Notes: In responding to and communicating about a specific reading, there are several things to keep in mind.
Reaction to blood glucose check results should always consider the student’s target range as it has been specified in the DMMP.
Not all children will have the same target range.
Even for an individual child, the target range may be somewhat different at different times of the day.
Take action for blood glucose levels that fall outside of students target range as per DMMP.
Avoid referring to the numbers as “good” or “bad,” both to the student and to others. The fact that the blood sugar is being checked is good, no matter what the results are. Refer to numbers as "in target", or "out of target“ or “below target” or “above target”.
Recognize value may vary according to time since eating, insulin, or physical activity.

## Slide 22: Module 4 Pre- and Post-Tests:
BLOOD GLUCOSE MONITORING
This tool may be freely duplicated and distributed for training purposes

## Slide 23
Which of the following can affect blood glucose levels?
  Insulin
  Food
  Physical Activity
  Stress/illness
  All the above
Blood glucose ranges are individualized for each student.
  True
  False
Students who are able to self-manage should be able to check their blood glucose in the classroom.
  True
  False
When should blood glucose levels be routinely checked?
  Every hour
  Before meals and snacks
  Every time student comes to the clinic
  According to the schedule in the student’s DMMP
  Never at school
Blood glucose levels are monitored using:
Urine test strip
Continuous glucose monitor
Glucose Meter
a and c
b and c

## Slide 24: Disclaimer
This presentation is not intended to provide legal or health care advice. Please consult with a legal or health care professional regarding your specific questions or needs.

## Slide 25: Where to Get More Information
AMERICAN DIABETES ASSOCIATION
1-800-DIABETES (342-2383)
DIABETES.ORG/SAFEATSCHOOL