## Slide 1: CONTINUOUS GLUCOSE MONITOR TECHNOLOGY
What Key Personnel Need To Know
Diabetes Care Tasks at School
Notes: The American Diabetes Association’s Diabetes Care Tasks at School: What Key Personnel Need to Know is a training curriculum that consists of PowerPoint modules with corresponding video segments, pre-/post-tests and other helpful resources.
This curriculum is based on and should be used in conjunction with the ADA’s Safe at School Guide “Helping the Student with Diabetes Succeed: A Guide for School Personnel”. Training participants should read the ADA Safe at School Guide in conjunction with this training gain a better understanding of the requirements for appropriate school diabetes care. The ADA’s Safe at School Guide and other training resources may be found www.diabetes.org/sastraining.
Some key points about the overall training:
Overall objective: The overall goal is to optimize safety, health, learning, and access for students with diabetes by providing diabetes education and training to school personnel o perform routine and emergency diabetes care tasks for students, under the supervision of a school nurse or another qualified health care professional. Completion of this training will help prepare school personnel to perform diabetes care tasks, ensuring that health needs are addressed in times and locations when a nurse is not available to provide needed care.
Rationale: The school nurse, when available, is the most appropriate person in the school setting to provide care for a student with diabetes. However, many schools do not have full-time nurses. Even for schools that do, the nurse may not always be available at all times during the school day, during school-sponsored extra-curricular activities or field trips to assist with routine care and emergency care. Trained school personnel must be available to perform and assist the student with diabetes care tasks.
PLEASE STATE: This presentation is not intended to provide legal or health care advice. Please consult with a legal or health care professional regarding your specific questions or needs.

## Slide 2: Optimal Student Health and Learning
Glucose monitoring is a vital piece of the Diabetes Medical Management Plan (DMMP).
GOAL:
Notes: Each training component was created specifically for school nurses and other qualified health care professionals to train school personnel.
These components are:
• Diabetes Basics
• Diabetes Medical Management Plan
• Hypoglycemia
• Hyperglycemia
• Blood Glucose Monitoring
• Continuous Glucose Monitoring
• Glucagon Administration
• Insulin Basics
• Insulin by Syringe and Vial
• Insulin by Pen
• Insulin by Pump
• Ketones
• Nutrition and Physical Activity
• After-School Programs, Sports and Camps
• Before- and After- School Care
• Childcare
• Psychosocial Aspects
• Legal Considerations
• Type 2 Diabetes
This unit is Continuous Glucose Monitoring.

## Slide 3: Learning Objectives
PARTICIPANTS WILL BE ABLE TO UNDERSTAND:
What is continuous glucose monitoring (CGM)
Why is CGM is used
When and how to use CGM information
Notes: Participants will be able to understand:
What is continuous glucose monitoring (CGM)
Why is CGM used
When and how to use CGM information

## Slide 4
CGMs have three parts: sensor, transmitter, and receiver.
CGM features vary slightly depending on the device
A tiny glucose-sensing device called a "sensor" is inserted just under the skin and remains for 7–14 days
A transmitter is attached to the sensor and sends the information to a receiver
The receiver may be a manufacturer-issued display device, smart device, or insulin pump
The system automatically records a glucose value every 1–5 minutes
Some CGMs provide alarms to signal when glucose is out of target range
What is CGM?
Notes: In the past few years considerable progress has been made in the continuous monitoring of glucose levels. The steps on the screen explain the basics of how the continuous monitoring or CGM technology works:
A tiny glucose-measuring device called a "sensor" is inserted just under the skin.
The sensor measures glucose in the tissue fluids several times a minute and sends the information to a phone-sized device.
The system automatically displays and records an average glucose value every one to five minutes and is worn for multiple days with duration depending on the manufacturer.
The state of the continuous monitoring technology is such that finger stick checks are still required at times for either calibration or treatment decisions. Glucose monitoring instruction will be outlined in the student’s DMMP.
Most CGM have alarms that signal when glucose is out of target range.
While continuous glucose monitors are becoming more common, they are still not used for all students with diabetes. Some individuals use them daily while others for a short period to give the health care providers a picture of what is happening with glucose levels between monitoring times, particularly after meals and at night while sleeping.
It’s important to remember that CGM features very depending on the manufacturer and model.

## Slide 5
CGM measures interstitial glucose, meaning the glucose concentration in the fluid just under the skin
This may lag 5-15 minutes behind the blood glucose
This may lead to some discrepancies between CGM readings and fingerstick readings, particularly if the glucose is changing rapidly
Current CGMs on the market have a high degree of accuracy based upon available data
What does a CGM measure?
Notes: CGM measures interstitial glucose, meaning the glucose concentration in the fluid just under the skin
This may lag 5-15 minutes behind the blood glucose
This may lead to some discrepancies between CGM readings and fingerstick readings, particularly if the glucose is changing rapidly
Current CGMs on the market have a high degree of accuracy based upon available data

## Slide 6
Can uncover undetected hypoglycemia and other glucose trends. Possible verification with finger-stick may be warranted.
Can provide direction and rate of change of glucose
Can provide alerts if glucose is or is predicted to be outside target range
Can contribute to improved glucose control and detecting the impact of food, activities and behavior on glycemia
Ongoing use is recommended to maximize benefits
May pair with select insulin pumps for automated insulin delivery systems
Can reduce the number of fingersticks
Why is CGM Used?
Notes: CGM is used to provide both real-time and retrospective glucose information to students, parents/caregivers and their healthcare providers.
CGM is well documented to uncover undetected hypoglycemia and other glucose trends to better adjust insulin doses and other management routines.
Direction and rate of change information as well as the glucose alerts contribute to earlier identification of low glucose in users who cannot recognize or communicate low glucose symptoms. User data and data sharing can also contribute to patient and caregiver reported quality of life.
CGM use has been documented in the literature to improve glucose control and for those on CGM therapy, ongoing and frequent use is recommended to maximize its benefits.

## Slide 7
DEXCOM G7 Trend Arrows
What do the arrows means?
Increasing/decreasing less than 1 mg/dL each minute
Glucose could increase/decrease 30-60 mg/dL in 30 minutes
Glucose could increase/decrease 60-90 mg/dL in 30 minutes
Glucose could increase more than 90 mg/dL in 30 minutes
Notes: This slide shows examples of trend arrows on the Dexcom G7. The trend arrows are visual indicators on the device’s display that show the direction and speed at which the blood glucose is changing.

## Slide 8
CGM settings are prescribed by the health care provider with input from the student and parents/guardians
Some CGMs are capable of sharing data real-time with caregiver(s) remotely
  Data sharing while in school should be specified in the student's 504 Plan
Severe low glucose (<54 mg/dl) is an acute risk and is an audible alarm that cannot be turned off.
  Other alarms are usually used conservatively to avoid unnecessary disruption of the student’s school activities
CGM Alarms
Notes: CGM settings are determined by the student, parent/guardian, and health care provider.
Some CGM are capable of sharing data real-time with the caregiver(s) remotely and CGM use has since increased rapidly, particularly in the pediatric population. The student should have access to their CGM receiver at all times and real-time data sharing with caregiver(s) and/or with school staff should be specified in the student’s 504 Plan.
Since hypoglycemia is an acute risk, CGM alarms for hypoglycemia will usually be set as audible alarms and commonly the low alert is recommended at 80. Other alarms are usually used conservatively to avoid unnecessary disruption of the student’s school activities but all settings are individualized per DMMP.

## Slide 9
If the CGM alarms for a low or high glucose, follow the instructions in the student’s DMMP to determine treatment
  Certain CGMs are approved for insulin dosing. Use of the CGM for treatment decisions should be specifically stated in the DMMP
Students identified as capable of managing diabetes independently may choose to respond to alarms and provide treatment without assistance
Students who cannot self-manage independently will require help responding appropriately to CGM alarms
All students, regardless of level of independence, may require assistance when they experience hypoglycemia.
CGM Alarms and How to Respond
Notes: School personnel should be prepared to respond to CGM alarms. If the CGM alerts for a low or high glucose, a blood glucose should be obtained to determine treatment, per DMMP. CGM data should not be used to make treatment decisions unless specifically stated otherwise in the DMMP.
The DMMP will have identified if the student is, or is not, capable of independent diabetes management and those who cannot self-manage will require help responding appropriately to CGM alarms.
However, all students, regardless of level of independence, will require assistance during severe hypoglycemia.

## Slide 10
Most CGMs are FDA-approved for treatment decisions, but not all
  Indications vary depending on product
  Even if FDA-approved, the student’s provider may still require blood glucose monitoring. For example:
    Confirming a low sensor glucose
    Confirming a very high sensor glucose
    Obtaining a blood glucose when the child has symptoms which do not match the CGM reading
Blood glucose levels should be monitored with a blood glucose meter in accordance with the student’s DMMP
Use Blood Glucose METER or CGM?
Notes: A student who wears a continuous glucose monitor to school still needs to check blood glucose with a regular meter before treatment; unless specifically stated otherwise in the DMMP.
Most CGM are now FDA approved for treatment decisions. However, not all are approved and some are only for certain ages. Given the rapid changes in diabetes technology, the student’s DMMP should always be consulted before using CGM or sensor data to make treatment decisions. Even if the student is using an FDA approved device for treatment decisions, they may not have permission from their provider to do so. Use CGM in accordance with manufacturer’s instructions and the student’s DMMP.

## Slide 11
Specific guidelines for CGM use should be outlined in the student’s DMMP
Based on FDA guidelines, criteria for the Dexcom G6 and G7 and FreeStyle Libre 2 and Libre 3 devices include:
  The receiver/smart device must display both a glucose value AND a trend arrow
    Important: Glucose readings are visible on the Libre2 reader only AFTER the user scans the sensor with the actual reader device or compatible smart phone
    Both devices are FDA-approved for treatment decisions
However, check student’s blood glucose with a fingerstick if the student is having symptoms that do not match the CGM’s data
Criteria for using CGM for treatment decisions
Notes: Specific guidelines for student’s using CGM for treatment decision, rather than blood glucose, should be outlined in the student’s DMMP. CGM systems approved for treatment decisions, like the Dexcom G6 and FreeStyle Libre2 and 3 have specific criteria that should be met. Older systems and those not FDA approved for treatment decisions will not be discussed here and recommendations for use will vary depending on the system.
Based on FDA guidelines, the Dexcom G6 and FreeStyle Libre2 data can be used to make treatment decisions without confirmation by blood glucose meter as long as the following criteria are met.
The student’s receiver (Dexcom receiver, Dexcom mobile app or FreeStyle Libre2 reader) must display both a glucose value AND a trend arrow
The student is not “stacking” insulin doses or rather taking insulin doses too close together
The student is not having symptoms contradictory to the sensor value
Other brand specific criteria include;
Dexcom G6:
Approved for 2-years and older
The student has not taken more than maximum acetaminophen doses as this can result in false high glucose values. Standard acetaminophen recommendations should not falsely affect the Dexcom G6.
FreeStyle Libre2 criteria:
Approved for 4-years and older
The student has not taken more than 500 mg of ascorbic acid per day as this can result in false high glucose values

## Slide 12
CGM and Treatment Decisions at School
MEALS
CGM values may be used to make treatment decisions if the conditions on the previous slide have been met and the student’s DMMP states the student can use the device to make treatment decisions
HYPOGLYCEMIA (LOWS)
If the student feels low or if the CGM displays < 70 mg/dl, check blood glucose with a blood glucose meter and treat according to meter value, per DMMP
If the CGM displays low, but the student is not symptomatic check blood glucose with a blood glucose meter and treat according to meter value, per DMMP.
HYPERGLYCEMIA (HIGHS)
CGM values may be used to make treatment decisions if the conditions on the previous slide have been met and the student’s DMMP states the student can use the device to make treatment decisions
  Specific guidelines should be outlined in the student’s DMMP. If not, use blood glucose meter for all treatment decisions
  These are general guidelines, follow DMMP for each student:
Notes: Before using CGM for treatment decisions at school there should be specific guidelines outlined in the student’s DMMP. If not, use blood glucose for all treatment decisions. Recommendations on CGM use will be determined by the student, parent/guardian, and health care provider. In general, recommendations for using CGM values for treatment decisions at school include meeting FDA recommendations but also:
Meals
For meal based correction boluses, the Dexcom G6 or FreeStyle Libre2 value may be used in place of using a blood glucose meter, per DMMP. However, the student’s DMMP may include specific details, in addition to FDA recommendations, regarding when to use blood glucose vs. sensor values and may be individualized for each student.
Hypoglycemia
If a student feels that his/her blood glucose is low or if the CGM displays < 80, then check blood glucose with a meter and provide treatment, per DMMP.
If the CGM displays hypoglycemia, but the student is not symptomatic, confirm blood glucose with a meter, prior to treating. Treat according to the blood glucose meter value, per DMMP.
Remember that if a student is sent to the school nurse’s office, another person should accompany the student if hypoglycemic. If the student if hypoglycemic, treatment should be provided immediately without the need to travel to the clinic.
Hyperglycemia
The Dexcom or FreeStyle Libre2 value may be used for treatment, per DMMP. Certain hyperglycemia values may still require blood glucose with a meter before treatment and should be detailed in the DMMP.

## Slide 13
Sampling of CGM
Notes: A number of different CGM systems are on the market.
CGM manufacturers are often the best resource for training resources and education.
CGM Manufacturers:
FreeStyle: https://www.myfreestyle.com
Medtronic: https://www.medtronicdiabetes.com
Dexcom: https://www.dexcom.com

## Slide 14
In cases where the sensor/transmitter falls off (for example in PE), it should be placed in a secure place as designated in the student’s written plan. No part of the CGM should be discarded. Sensor placement requires training and is routinely done at home. As such, back-up CGM supplies may not be necessary at school (unless the student self-manages independently, per DMMP).
CGM Supplies at School
Receiver
Sensor and Transmitter
Alcohol Wipes
Skin prep wipes
(if used)
Inserter
(if used)
Manufacturer's manual, alarm card
Notes: Sensor placement requires training and is routinely done at home. However, if the parent/guardian prefers to maintain CGM supplies at school the following supplies should be provided by the parent/guardian and kept in a designated place at school:
Receiver
Transmitter (Some models have a combined receiver/transmitter unit)
Sensors
Alcohol wipes
Skin prep wipes (if used)
Inserter (if used)
Manufacturers manual, alarm card
In cases where the sensor/transmitter falls off (for example in PE) it should be placed in a secure place as designated in the student’s written plan. No part of the CGM should be discarded. Sensor placement requires training and is routinely done at home but students who have been identified as capable of managing independently may carry CGM supplies for immediate site change as necessary.

## Slide 15: Module 5 Pre- and Post-Tests:
CONTINUOUS GLUCOSE MONITOR TECHNOLOGY
This tool may be freely duplicated and distributed for training purposes

## Slide 16
Which CGM alarm cannot be turned off?
  Out of insulin
  Hyperglycemia (high blood glucose)
  Severe hypoglycemia (low blood glucose)
  CGM alarms should always be on the vibrate mode
All CGMs are indicated for treatment decisions.
  True
  False
Which item below is NOT part of CGM’s equipment?
  Receiver
  Lancet
  Transmitter
  Sensors

## Slide 17: Disclaimer
This presentation is not intended to provide legal or health care advice. Please consult with a legal or health care professional regarding your specific questions or needs.

## Slide 18: Where to Get More Information
AMERICAN DIABETES ASSOCIATION
1-800-DIABETES (342-2383)
DIABETES.ORG/SAFEATSCHOOL